## Slide 1: NPN-NMOS Transistor tracer
Dave Ve3OOI
march 2023
“I have not failed. I’ve just found 10,000 ways that won’t work"
Thomas Edison
This Project is a Textbook Example of Making Mistakes

## Slide 2: The problem
You have a load that needs 350mA of current to work properly.
  What transistor should you use?
  What base resistor do you need to drive 100mA?
You need to have a quiescent current of 200mA through a MOSFET.
  What bias do you apply to the MOSFET to get 200mA?
You need to have a reverse voltage protection diode with lowest voltage drop.
  Which diode do you use from a bag of diodes you ordered from Digikey.
You are building a Class A RF amplifier and you need to set the bias point of the transistor so that it 100% linear.
  What is the optimum bias point to use?
  What base current do you need to get the desired output current?

## Slide 3: AGENDA
  The Transistor Tracer Hardware Version 1
  Python Graphing Program
  Summary of Various Transistor Curves (Not a Tutorial)
  Data Sheet Comparison with Transistor Tracer Graphs
    Diodes
    NPN Transistors
    Enhancement Mode MOSFETS
  Changes in Version 2
This is not a Transistor Tutorial. Its assumed you understand how a BJT and MOSFET operates and terms (e.g., Vbe, Vgs, Vce, Vds, etc). Only a short summary if given

## Slide 4: TRANSISTOR TRACER V1 evolution
Drop PNP and PCHAN MOS Functionality

## Slide 5: How it works
Use Arduino ADC to measure voltage difference and measure Vce, Vcc, Ic
Use Arduino ADC to measure voltage difference and measure Vbe, Ib, Vb
Use Arduino PWM and a LPF to generate a DC voltage
Pots uses as a resistive divider to keep ADC voltages below 5V

## Slide 6: SCHEMATIC
462

## Slide 7: version 1: Speeds and feeds
  NPN BJTs with EBC, BEC, BCE
  NMOS (N Channel Enhancement Mode MOSFET) with GDS, GSD, DGS
  Vcc 14V, Max Collector/Drain Voltage: 10@930mA
  Max Base/Gate voltage: 4.3@7mA

## Slide 8: PC Interface – python Microcontroller Console

## Slide 9: Microcontroller console
  Data acquisition program written in python for PC
    https://github.com/drajnauth/uC_Console
  Used to acquire and plot data from a microcontroller
  Data is needs to be written to serial console in a specific format
    Data to be captures has “#” at start of line
    Finish data set with a “|”
    Create a new series with a “=“
  Currently supports
    Plot after all data received: x-y plots, s-x-y series
    Plot as data arrives (live plot): y, x-y, s-x-y
X-Y
S-X-Y
YOU MUST PROGRAM uC TO SEND DATA

## Slide 10: Microcontroller console: connection
Enter command to be sent to uC
(same as Arduino Serial Console)
Serial Ports available to connect to
Select com port from drop down
Select baud rate from drop down box
Select the “connect” checkbox to connect to the uC

## Slide 11: Microcontroller console: usage
Connection successful message
Text from uC is black. Text from program is blue
Select if you want to save data to a csv file or plot the data
Select the type of plot or the data series to save to csv file
When data has been successfully captures, the “GO” button will be enabled and you can press “GO” to generate the plot or save the csv file

## Slide 12: HOW it works
:> tni32
Rc = 32.00
:> BJT Input Sweep
Sweeping Vb 0.00 V to 4.60 V
Vc/Vd: 4.6000 Vb/Vg 0.0000 - 4.60 inc 0.23
#0.00000000000000000000,0.000000000000
#0.18862840652465820312,0.000000000000
#0.43115062713623046875,0.000000000000
#0.66019940376281738281,0.006315693378
#0.71409320831298828125,0.044209775924
#0.74104013442993164062,0.077472376823
#0.75451364517211914062,0.093472108840
#0.78146052360534667968,0.103577196598
#0.78146052360534667968,0.111156010627
#0.79493398666381835937,0.118313789367
#0.80840740203857421875,0.124629485607
#0.80840740203857421875,0.130103087425
#0.82188091278076171875,0.135576665401
#0.82188091278076171875,0.140208148956
#0.83535432815551757812,0.145260715484
#0.83535432815551757812,0.149471163749
#0.83535432815551757812,0.153260574340
#0.84882774353027343750,0.157049989700
#0.84882774353027343750,0.160418343544
#0.86230125427246093750,0.163365659713
|
:>
Plotting Enabled for x,y Data
tni32
Rc = 32.00
:> BJT Input Sweep
Sweeping Vb 0.00 V to 4.60 V
Vc/Vd: 4.6000 Vb/Vg 0.0000 - 4.60 inc 0.23
Captured: 0.0, 0.0
Captured: 0.1886284065246582, 0.0
Captured: 0.4311506271362305, 0.0
Captured: 0.6601994037628174, 0.005473584175
Captured: 0.7140932083129883, 0.043788747787
Captured: 0.7410401344299317, 0.077472376823
Captured: 0.7545136451721192, 0.093472118377
Captured: 0.7814605236053467, 0.103998255729
Captured: 0.7814605236053467, 0.111577057838
Captured: 0.7949339866638183, 0.118734836578
Captured: 0.8084074020385742, 0.125050520896
Captured: 0.8084074020385742, 0.130524110794
Captured: 0.8218809127807617, 0.135576665401
Captured: 0.8218809127807617, 0.140629196166
Captured: 0.8353543281555176, 0.145681738853
Captured: 0.8353543281555176, 0.149471163749
Captured: 0.8353543281555176, 0.153681621551
Captured: 0.8488277435302735, 0.1570499897
Captured: 0.8488277435302735, 0.160418367385
Captured: 0.862301254272461, 0.163365659713
Captured 20 data pairs for 0 series. Press 'GO' to plot
:>
The Microcontroller must have a CLI
The uC must append “#” to numbers and send other control characters
# // x,y numbers
| // end control characters
= // switch control character
// i.e., new xy plot)

## Slide 13: HOW it works
The Microcontroller must have a CLI
The uC must append “#” to numbers and send other control characters
# // x,y numbers
| // end control characters
= // switch control character
// i.e., new xy plot)
tno 32
Rc = 32.00
:> BJT Output Sweep
Sweeping Vb 0.00 V to 4.60 V
BJT NPN Output Sweep
Vb 0.0000 - 2.3000
Vc 0.0100 - 4.6000
#0.000000000000,0.000000000000,0.000000000000
#0.000000000000,0.848827743530,-0.000421045351
#0.000000000000,1.724602460861,0.000000000000
=
#0.000013473452,0.000000000000,0.000000000000
#0.000000000000,0.848827743530,-0.000421045351
#0.000000000000,1.724602460861,0.000000000000
=
#0.000013473480,0.000000000000,0.000000000000
#0.000013473480,0.835354328155,0.000000000000
#0.000013473480,1.724602460861,-0.000421043491
=
#0.000080840768,0.000000000000,0.000000000000
#0.000040420351,0.026946914196,0.001263136625
#0.000026946902,0.579358625411,0.004631500720
=
#0.000242522192,0.000000000000,0.000000000000
#0.000229048728,0.000000000000,0.000842091083
#0.000161681470,0.107787656784,0.017683911323
=
#0.000431150627,0.000000000000,0.000000000000
#0.000417677164,0.000000000000,0.000842091083
#0.000377256870,0.067367286682,0.019368094444
=
#0.000646725940,0.000000000000,0.000000000000
#0.000633252525,0.000000000000,0.000842091083
#0.000579358673,0.053893828392,0.019789141654
=
|
:>
Series Id (not used to plot)
X data point
Y data point
Switch to new XY plot
End of data. Enable plot

## Slide 14: CLI Manual

## Slide 15: Arduino software (firmware)
This software was compiled using PlatformIO IDE. As is it will NOT compile with Arduino IDE.
For Arduino IDE, simply rename the main.cpp to an Arduino program name (*.ino). Then create a directory with the same name and store all .cpp and .h files in that directory

## Slide 16: Arduino IDE vs PLATForm.IO
Arduino PlatformIO
RAM 1689 1414
FLASH 23334 19098

## Slide 17: CLI Guide: SUMMARY
H // Help – Command summary
C // Display current Calibration
C [R|M|D] // Calibrate
D // Set default values
E [I|P] // Configure EEPROM
M [R] // Measure Voltages
P [3|10 [255] // Set PWM on pin 3 or pin 10
R // Reset
S [V] [B|C] [O] [mV] // Set voltage on Base or Vcc pin.
S [I] [uA] // Set current on Base
S [U] [D|M|U] // Set default unit to decimal, Milla or Micro for currents
S [M] [B|C] [min] [max] // Set min max voltage to sweep
S [R] [B|C] [R] // Set Rb or Rc resistor values
S [P] [B|C] [n] // Set number of data point in sweep between max and min
T [NI|NIV|NO|NB|NBC|NR|NG] // Trace NPN Transistor
T [FI|FIV|FO|FK|FG|FR] // Trace N Chan MOSFET
T [DI|DO] // Trace Diode

## Slide 18: CLI Guide: Calibration
Display current Calibration values
C
Connect the Tracer to Vcc with empty socket (nothing connected) to determine the voltage sweep range for base/gate voltage and collector/drain voltage. It also calculated the conversion constant to convert collect/drain (pin 10) PWM voltage to actual output Vcc voltage delivered to DUT
C M
Connect the Tracer to Vcc with empty socket (nothing connected) to determine the voltage sweep range for base/gate voltage and collector/drain voltage. It also calculated the conversion constant to convert collect/drain (pin 10) PWM voltage to actual output Vcc voltage delivered to DUT
C D
Connect the Tracer to Vcc with empty socket (nothing connected). It generates a PWM voltage on collector/drain pin defined by a calibration voltage constant (see below) and then measures and displays all ADC values 10 times. This is one way to calibrate ADC pots.
C R

## Slide 19: Calibration & CONFIGURATION for Version 1
Before powering up Arduino, you need to calibrate pots to not damage the Arduino.
Remove Arduino. Remove jumpers from all trim pots jumper headers pins.
Measure the voltage at the +5V terminal pin (J7).
Connect a jumper wire from +5V terminal to each pot’s jumper “+” pin (J1, J2, J6, J7). “+” is marked on the silkscreen
Adjust each pot until you get 1.75V output (exactly) at the pot’s wiper. Use one consistent VOM.
Insert Arduino and load the code. Power up.
Connect via TTY console to Arduino. Enter the C R command to display all ADC values from each pot
Note that each pot has ADC1, ADC2, ADC3, ADC4 marked on the silkscreen. Each jumper associate with the pot is marked as AD1, AD2, AD3, AD4. This corresponds to the ADC number on the Arduino.
Connect 5V to the same jumper in step 3. Note the ADC number of the jumper and pot.
  Adjust the pot’s wiper (very fine adjust needed) until the corresponding ADC displayed by the Arduino is 364. Repeat for all jumpers/pots.
  Enter the R command to reset the Arduino when done
Complete and record the following calculations for each pot:
  Calculate VOLTAGE_DIVIDER = V(wiper)/V(applied) e.g., 1.75/5 = 0.357
  Calculate ADC_CONVERSION = ADC_Value/V(wiper) e.g., 364/1.75 = 208.0
  Calculate VOLTAGE_CONVERSION = VOLTAGE_DIVIDER * ADC_CONVERSION e.g., 0.357*208 = 78.0
Take the average VOLTAGE_CONVERSION and update the #define ADC_CONVERSION ((float)78.0) in the defines.h file
You need to measure the resistance of the Base and Collector resistors. Update the following defines in the defines.h file
  #define RC_RESISTORHIGH 32
  #define RC_RESISTORLOW 10
  #define RB_RESISTORLOW 462
Compile and load the Arduino program before continuing. The above defines must be in place.
Complete the following. DO NO RESET OR POWER OFF ARDUINO UNTIL ALL STEPS ARE COMPLETE. Failure will result in redoing below
  Set the base resistor value using the S R B nnnn command where nnnn is the resistor value. E.g., S R B 462
  Set the jumper J4 (RCSEL) to the resistor for the sweep. Use the S R C nnnn command to define the Collector resistor nnnn that the jumper selected. E.g., S R C 10
  With Vcc applied and nothing connected to the ZIF socket (socket is empty), run the C M command to have the Arduino figure out the max voltages available to it during a sweep. If you change Vcc, this needs to be repeated.
  Update the EEPROM with the configuration by entering the E W command. Once completed, the Arduino will power up with these values.
Your transistor curve trace (V1) is now ready.

## Slide 20: Operation: SWEEPS
The transistor tracer sweeps a set of PWM voltages.
  There is a base/gate PWM voltage (Pin 3) that is applied directly to the transistor under test.
  There is a Vcc PWM voltage (Pin 10) that is amplified by an opamp and a high-power transistor
Since the base/gate PWM voltage is fed directly to the transistor under test, the base/gate voltage is essentially the output voltage to the transistor
However, since the Vcc PWM voltage is amplified, the output voltage fed to the collector/drain of the transistor under test is different.
When sweeping Vcc values, only the PWM voltage is used. When you set voltage ranges, you are setting the PWM voltage that the Arduino outputs.
You can manually set the output voltage supplied to the transistor under test using the S V command. However, this is a one-time setting. Its not used in a sweep. BE CAREFULL SETTING VOLTAGES MANUALLY – you could destroy a resistor or the transistor under test if you exceed its maximum ratings
REMEMBER: When you set voltage ranges, you are setting the PWM voltage that the Arduino outputs. You are NOT setting the output voltage fed to the transistor under test

## Slide 21: Operation: NPN Sweeps
The T command is used to complete Traces. The T N command is used to complete NPN Transistor traces
The following traces uses the configured min and max voltages. You can adjust sweep voltages and number of data points (resolution) to be taken during a sweep. Use the S M command to adjust min & max voltages for and S P to set data points.
The following below outlines the various traces:
Input Trace: T N I
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the base voltage from configured min to max at define inc (resolution). It prints out Vbe vs Ic
Input Trace: T N I V
  This command is the same as above except it prints out Vbe vs Vce
Output Trace: T N O
  This command sweeps the base voltage from configurated min to max with inc. For each base voltage, it then sweeps Vcc from configured min to max at defined inc. For each base voltage it print out Vce vs Ic in the form Ib, Vce, Ic
Beta Trace: T N B
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the base voltage from configured min to max at define inc (resolution). It calculates transistor beta and prints out Ib vs Beta
Beta Trace: T N B C
  This command is the same as above except it prints out prints out Ic vs Beta
Beta Trace: T N R
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the base voltage from configured min to max at define inc (resolution). It calculates transistor re (intrinsic resistance) and prints out Ic vs re
Beta Trace: T N G
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the base voltage from configured min to max at define inc (resolution). It calculates transistor transconductance and prints out Ic vs gm

## Slide 22: Operation: N-CHANNEL enhancement mode MOSFET Sweeps
The T command is used to complete Traces. The T F command is used to complete N channel Mosfet traces
The following traces uses the configured min and max voltages. You can adjust sweep voltages and number of data points (resolution) to be taken during a sweep. Use the S M command to adjust min & max voltages for and S P to set data points.
The following below outlines the various traces:
Input Trace: T F I
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the gate voltage from configured min to max at define inc (resolution). It prints out Vgs vs Id
Input Trace: T F I V
  This command is the same as above except it prints out Vgs vs Vds
Output Trace: T F O
  This command sweeps the base voltage from configurated min to max with inc. For each gate voltage, it then sweeps Vcc from configured min to max at defined inc. For each gate voltage it print out Vds vs Id in the form Id, Vgs, Id
Intrinsic Resistance Trace: T F R
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the gate voltage from configured min to max at define inc (resolution). It calculates transistor re (intrinsic resistance) and prints out Id vs Rds
Transconductance Trace: T F G
  This command sets the Vcc voltage to the maximum available voltage and then sweeps the gate voltage from configured min to max at define inc (resolution). It calculates transistor transconductance and prints out Id vs gm
Transconductance Trace: T F G
  This command is the same as above except it it calculates transistor transconductance constant K and prints out Id vs K

## Slide 23: Operation: diode Sweeps
The T command is used to complete Traces. The T D command is used to complete diode traces
The following traces uses the configured min and max voltages. You can adjust sweep voltages and number of data points (resolution) to be taken during a sweep. Use the S M command to adjust min & max voltages for and S P to set data points.
Note that the diode MUST be oriented correctly in the socket.
The following below outlines the various traces:
Input Trace: T D I
  The diode must be connected between the base/gate socket and ground. The cathode is connected to emitter/source socket (ground). For a Zener diode, its reversed, the cathode is connected to the base. This command sets the Vcc voltage to the maximum available voltage and then sweeps the base/gate voltage from configured min to max at define inc (resolution). It prints out Vb vs Id
Output Trace: T D O
  The diode will need a resistor connected between the cathode and the emitter/source socket (ground). The resistor is selected to NOT exceed the maximum current the diode can handle. The resistor also protect the Arduino pin used for base PWM output (pin 3). Failure to add a resistor could cause damage to the Arduino. This command set the base/gate voltage Arduino pin to zero to sink current. It then sweeps the Vcc voltage from configurated min to max with inc. For each Vcc voltage, it measure the voltage drop across the collector/drain to the base/gate sockets along with current. It print out Vf vs I
Special Jig Required for Output Seep

## Slide 24: Operation: custom sweeps
The S command is used to set trace values.
For base/gate voltage there is a min voltage, max voltage
Its sets the PWM voltage output from the Arduino. IT DOES NOT SET THE ACTUAL OUTPUT VOLTAGE DELIVERED TO THE DUT
Values MUST be entered as milla volts (mV) e.g., 4V entered at 4000
The following below outlines the various configuration options:
Base/Gate Sweep: S M B xxxx yyyy
  This command sets the minimum voltage (xxxx) and the maximum voltage (yyyy) for the base/gate PWM pin. The increment use for trace is automatically calculated to the number of data point defined. Default is min: 0 and maximum determined by C M calibration command.
Vcc Sweep: S M C xxxx yyyy
  This command sets the minimum voltage (xxxx) and the maximum voltage (yyyy) for the Vcc PWM pin. The increment use for trace is automatically calculated to the number of data point defined. Default is min: 0 and maximum determined by C M calibration command.
You need to enter the E W command to update the EEPROM configuration values or else these definition will be lost at next restart of the Arduino

## Slide 25: Operation: custom sweeps
The S command is used to set trace values.
You can configure the number of data point to be taken during a typical sweep. Some sweeps such as the beta, gm, K and Rds and re sweeps typically take 25% of the increment.
Example:
  If the min is 0.01V and the max is 4.6V
  If you set the number of point to 10, then the increment uses during a sweep is (4.6 – 0.01)/20 = 0.45
  Therefore, duing a sweep, 10 measurements are taken with each increasing by 0.45V from min to max.
The following below outlines the various configuration options:
Base/Gate Sweep: S P B xxxx
  This command sets the number of data points to measure during a sweep of the base/gate voltage. The increment used for sweep is automatically calculated. Default is 10 data points for base/gate.
  The range of allowed data points is defined in the defines.h file as:
    #define MIN_NUM_VB_VOLTAGE 5
    #define MAX_NUM_VB_VOLTAGE 20
    #define NUM_VB_VOLTAGE 10 // Default number of points
Vcc Sweep: S P C xxxx
  This command sets the minimum voltage (xxxx) and the maximum voltage (yyyy) for the Vcc PWM pin. The increment use for trace is automatically calculated to the number of data point defined. Default is 15 data points for Vcc.
  The range of allowed data points is defined in the defines.h file as:
    #define MIN_NUM_VC_VOLTAGE 5
    #define MAX_NUM_VC_VOLTAGE 20
    #define NUM_VC_VOLTAGE 15 // Default number of points
You need to enter the E W command to update the EEPROM configuration values or else these definition will be lost at next restart of the Arduino

## Slide 26: Operation: EEPROM MANAGEMENT
The E command is used to manage configuration values stored in the EEPROM.
Configuration values stored in the EEPROM will be restored whenever the Arduino is power on.
The following below outlines the various configuration options:
Read EEPROM: E R
  This command reads and overwrite the current running configuration with the configuration stored in the EEPROM. Any unsaved changes will be lost (i.e., changes to voltage ranges, points, resistor vales, max voltages, etc)
Write EEPROM: E W
  This command write the current configuration to the EEPROM. It overwrites the EEPROM.
Initialize EEPROM: E I
  This command sets the default configuration values, calculates the max voltages and then write the default configuration to the EEPROM. Think of this as a factory reset.

## Slide 27: Operation: MISC MANAGEMENT
There are a few other MISC command that can be used:
Set Voltages: S V B xxxx or S V C xxxx
  This set the PWM voltage at pin 3 (base voltage) and pin 10 (Vcc voltage). The voltage is given by xxxx and is in milla volts (i.e., mV). If O (Oh and not zero) is added after the B or C then, the Arduino tries to set the output voltage delivered to the transistor under test. Note that this value could be off by up to 0.5 volts.
Set PWM: P xx yyy
  This command manually sets the PWM output of pin 3 or pin 10 of the Arduino and is used for troubleshooting. Xx is the pin number (3 or 10) and yyy is the PWM value (1-255). A higher PWM values will output a higher voltage.
Reset Arduino: M
  This reads and display all the voltages and currents. It assumed you have manually set a voltage using the P or V commands
Reset: R
  This resets the Arduino. Its not the same as a power on.
Set Defaults: D
  This command sets the default parameter to the running config. It does not change the EEPROM config.
Set current units for graph: S U D or S U M or S U U
  This command sets units for current values produced. S U D is used for normal decimal, S U M is used for milla and S U U is used for micro

## Slide 28: Measurements of NPN BJT Transistors

## Slide 29: If you are looking for a TUTORIAL…
MOS FET Modification Transistor Curve Tracer HeathKit
https://www.youtube.com/watch?v=rFmDUPVdYSc&t=4953s
W2AEW: Back to Basics: Basics of the Bipolar Transistor - NPN and PNP
https://www.youtube.com/watch?v=IrAUC4ZoNYY&t=1263s
Microelectronic Prof. Tony Chan Carusone: Transistor Amplifier Basic Principles
https://www.youtube.com/watch?v=IrAUC4ZoNYY&t=1263s
Mateo Aboy: Series of Videos on BJT and FET Amplifiers
https://www.youtube.com/playlist?list=PLZvLSclgk4yJkRHB_eJ10zo2exTY_irR0
Electronics with Professor Fiore: Semiconductor Devices
https://www.youtube.com/playlist?list=PLxuejeK2BP_dtn1ijj1lZKrIs2gHPPsyp

## Slide 30: transconductance
A voltage applied at the input causes a current at the output.
Transconductance is a measure of the slope. It’s like a “transfer function”
This is a very important concept for MOSFETS
It is used with NPN Transistors, but they are more a current device

## Slide 31: Transistor operation
Feed Small
Current into Base
Get a LARGE current between Collector and Emitter
NPN TRANSISTOR
Datasheets today use hfe instead of Beta. Beta sounds “cooler”
Feed
Voltage above Threshold
Get a LARGE current between Drain and Source
NMOS TRANSISTOR
gm
NPN
N-CH
MOSFET

## Slide 32: Transistor regions: voltage & current

## Slide 33: Transistor REGIONS: Current
Vbe(th)
Vbe(sat)
Amplification
No Amplification
Feed Small
Current into Base
Get a LARGE current between Collector and Emitter
TRANSISTOR
  There is “Vbe(th)” for BJT, which is the threshold voltage (actually current) at which device starts conducting. Not specified on data sheet!!
  There is Vbe(sat) for BJT, which is the maximum voltage at which collector current is constant.
Beta is not constant

## Slide 34: Transistor REGIONS: voltage
0
Vce=Vout
Vcc
Vbe(th)
Cutoff
Region
Active Region
small
large
Vbe(sat)
Vce(cutoff)
Saturation Region
Vbe

## Slide 35: NPN Plots
Ib vs Beta
Ic vs Beta
Vbe vs Ic
Ib: Vce vs Ic
Ib
Ic
Vce
Ic
Ic
Ib
Vbe vs Vce
Vce
Beta
Beta
Vbe
Vbe

## Slide 36: NPN Plots
Vbe vs re
Vbe
re
Vbe vs gm

## Slide 37: Measurements of diodes and BJT devices

## Slide 38: DIODE PLOTS: 1N914
V vs I
Vcc(i) vs Vf
Special Jig
Required
Vcc(i)
Vf

## Slide 39: DIODE PLOTS: 1n752 (5.6Z)
Vcc(i) vs Vf

## Slide 41: 2N2222A
Vbe (sat)?
190
Vbe vs Ic
Vbe vs Vce
Ic vs Beta
Active Region
Q
Q
0.9V
~ 0.8V
Actual roll over or Tracer Limitation

## Slide 42: 2n3904
190
260
200
MINIMUM
Vbe vs Ic
Vbe vs Vce
Ic vs Beta
Limit for Vbe

## Slide 43: BC337
0.73V
320
Ib vs Beta
Vbe vs Ic
Vbe vs Vce
~ 0.7V
Actual roll over or Tracer Limitation

## Slide 44: 2N2219A
112
~ 0.9V

## Slide 45: BD139
WTF – negative slope!!
Plot is Beta vs Ib
(Ib is being sweeped – i.e., increasing
Prior plot is Beta vs Ic
(Ic is an an independent variable)
Ib
Beta
PS Current Limit
500mA
Ic vs Beta
Ib vs Beta
Ic
Beta

## Slide 46: BD139
PS Current Limit
500mA
250
0.8V
PS Current Limit
500mA
~ 0.7V

## Slide 47: 2N3050
PS Current Limit
500mA
170
< 0.9V

## Slide 48: 2sc5706
PS Current Limit
500mA
280
~ 0.7V

## Slide 49: Measurements of n-channel enhancement MODE mosfets

## Slide 50: Transistor operation
Feed Small
Current into Base
Get a LARGE current between Collector and Emitter
NPN TRANSISTOR
Datasheets today use hfe instead of Beta. Beta sounds “cooler”
Feed
Voltage above Threshold
Get a LARGE current between Drain and Source
NMOS TRANSISTOR
gm
NPN
N-CH
MOSFET

## Slide 51: NMOS MOSFETS
Similar to BJT:
  There is Vbe(turn on) for BJT, there is Vgs(on) or Vgs(th). This is threshold voltage at which device starts conducting
  There is a maximum Vbe or Vgs where current is at maximum and constant. Vbe(sat) and Vgs(triode?). For MOSFET, Not specified on data sheet!!
NMOS

## Slide 52: MOSFET REGIONS: voltage
0
Vds=Vout
Vcc
Vgs(th)
Cutoff
Region
Active or
Saturation
Region
small
large
Vgs(triode)
Vds(cutoff)
Triode or Ohmic
Region
Vgs

## Slide 53: MOSFETS
Similar Input and Output charts to BJT:
  However, the input curve will show saturation if Vgs is high enough
No concept of Beta (current amplification). MOSFET is a voltage device. Voltage controls current.
The gain depends on gm (transconductance) and K
K is based on channel parameters inside MOSFET
Datasheets typically provide transconductance gm

## Slide 54: NMOS Plots
gm
Id
Id vs gm
Vgs vs Id
Vgs: Vds vs Id
Id
Id
Vgs
Vds
Vgs
Id vs k
Id
k
Id vs Rds
Id
Rds

## Slide 55: 2n7000
1.3V
350mS
2.5
Id vs gm
Vgs vs Id
Vgs: Vds vs Id
Saturation Region
Q

## Slide 56: BS170
1.50V
280mS
3.2V
Active Region

## Slide 57: IRF510
3.0V
0.5
Don’t have the drive to measure this MOSFET

## Slide 58: IRFZ20
3.30V
500mS
Don’t have the drive to measure this MOSFET

## Slide 59: RD16HHF1
Vgs vs Vds
Vgs vs Id
Id vs gm
Don’t have the drive to measure this MOSFET

## Slide 60: Issues
Need higher current and voltage for Vcc and Vb
  Voltage drop from Opamp and TIP120 (~8V)
  Using PWM (~4.3V) for Vb
Need better way to sweep Vcc/Vc
Need better socket for transistors

## Slide 61: Version 2
ZIF Socket
DC Voltage Amplifier

## Slide 62: version 2: Speeds and feeds
  NPN BJTs with EBC, BEC, BCE
  NMOS (N Channel Enhancement Mode MOSFET) with GDS, GSD, DGS
  Vcc 14V, Max Collector/Drain Voltage: 11.1@1.7A
  Vcc 14V, Max Base/Gate voltage: 11.1V@22mA
Version 1:
Vcc 14V, Max Collector/Drain Voltage: 10@930mA
Max Base/Gate voltage: 4.30@7mA